## Slide 1: Global Procurement - Supplier Quality Introduction to MSA
Lise Robert SQS (Supplier Quality Specialist)
Rev. 01 – Dec 17th 2018

## Slide 2: Introduction to Measurement System Analysis (MSA)
Everyday our lives are being impacted by more and more data. We have become a data driven society.
In business and industry, we are using data in more ways than ever before.
Today manufacturing companies gather massive amounts of information through measurement and inspection. When this measurement data is being used to make decisions regarding the process and the business in general it is vital that the data is accurate. If there are errors in our measurement system we will be making decisions based on incorrect data. We could be making incorrect decisions or producing non-conforming parts. A properly planned and executed Measurement System Analysis (MSA) can help build a strong foundation for any data based decision making process.

## Slide 3: What is Measurement System Analysis (MSA)
MSA is defined as an experimental and mathematical method of determining the amount of variation that exists within a measurement process. Variation in the measurement process can directly contribute to our overall process variability. MSA is used to certify the measurement system for use by evaluating the system’s accuracy, precision and stability.

## Slide 4: What is a Measurement System?
Before we dive further into MSA, we should review the definition of a measurement system and some of the common sources of variation. A measurement system has been described as a system of related measures that enables the quantification of particular characteristics. It can also include a collection of gages, fixtures, software and personnel required to validate a particular unit of measure or make an assessment of the feature or characteristic being measured.

## Slide 5: What is a Measurement System?
Variation Think of Measurement as a
Process

## Slide 6: What is a Measurement System?
Measurement
The assignment of numbers to material things to represent the relationships among them with respect to particular properties.
C. Eisenhart (1963)

## Slide 7: What is a Measurement System?
The sources of variation in a measurement process can include the following:
Process – test method, specification
Personnel – the operators, their skill level, training, etc.
Tools / Equipment – gages, fixtures, test equipment used and their associated calibration systems
Items to be measured – the part or material samples measured, the sampling plan, etc.
Environmental factors – temperature, humidity, etc.

## Slide 8: What is a Measurement System?
All of these possible sources of variation should be considered during Measurement System Analysis. Evaluation of a measurement system should include the use of specific quality tools to identify the most likely source of variation. Most MSA activities examine two primary sources of variation, the parts and the measurement of those parts. The sum of these two values represents the total variation in a measurement system.

## Slide 9: Why Perform Measurement System Analysis (MSA)
An effective MSA process can help assure that the data being collected is accurate and the system of collecting the data is appropriate to the process.
Good reliable data can prevent wasted time, labor and scrap in a manufacturing process.

## Slide 10: Why Perform Measurement System Analysis (MSA)
A major manufacturing company began receiving calls from several of their customers reporting non-compliant materials received at their facilities sites. The parts were not properly snapping together to form an even surface or would not lock in place.
The process was audited and found that the parts were being produced out of spec. The operator was following the inspection plan and using the assigned gages for the inspection. The problem was that the gage did not have adequate resolution to detect the non-conforming parts.
An ineffective measurement system can allow bad parts to be accepted and good parts to be rejected, resulting in dissatisfied customers and excessive scrap. MSA could have prevented the problem and assured that accurate useful data was being collected..
Example

## Slide 11: How to Perform Measurement System Analysis (MSA)
MSA is a collection of experiments and analysis performed to evaluate a measurement system’s capability, performance and amount of uncertainty regarding the values measured. We should review the measurement data being collected, the methods and tools used to collect and record the data.
Our goal is to quantify the effectiveness of the measurement system, analyze the variation in the data and determine its likely source. We need to evaluate the quality of the data being collected in regards to location and width variation. Data collected should be evaluated for bias, stability and linearity.

## Slide 12: How to Perform Measurement System Analysis (MSA)
During an MSA activity, the amount of measurement uncertainty must be evaluated for each type of gage or measurement tool defined within the process Control Plans.
Each tool should have the correct level of discrimination and resolution to obtain useful data. The process, the tools being used (gages, fixtures, instruments, etc.) and the operators are evaluated for proper definition, accuracy, precision, repeatability and reproducibility.

## Slide 13: How to Perform Measurement System Analysis (MSA)
Data Classifications
Prior to analyzing the data and or the gages, tools or fixtures, we must determine the type of data being collected. The data could be attribute data or variable data.
Attribute data is classified into specific values where variable or continuous data can have an infinite number of values.

## Slide 14: How to Perform Measurement System Analysis (MSA)
The Master Sample
To perform a study, you should first obtain a sample and establish the reference value compared to a traceable standard. Some processes will already have “master samples” established for the high and low end of the expected measurement specification.

## Slide 15: How to Perform Measurement System Analysis (MSA)
The Gage R&R Study
For gages or instruments used to collect variable continuous data, Gage Repeatability and Reproducibility (Gage R & R) can be performed to evaluate the level of uncertainty within a measurement system.

## Slide 16: How to Perform Measurement System Analysis (MSA)
To perform a Gage R & R, first select the gage to be evaluated.
Then perform the following steps:
  Obtain at least 10 random samples of parts manufactured during a regular production run
  Choose three operators that regularly perform the particular inspection
  Have each of the operators measure the sample parts and record the data
  Repeat the measurement process three times with each operator using the same parts
  Calculate the average (mean) readings and the range of the trial averages for each of the operators
  Calculate the difference of each operator’s averages, average range and the range of measurements for each sample part used in the study
  Calculate repeatability to determine the amount of equipment variation
  Calculate reproducibility to determine the amount of variation introduced by the operators
  Calculate the variation in the parts and total variation percentages

## Slide 17: How to Perform Measurement System Analysis (MSA)
The resulting Gage R & R percentage is used as a basis for accepting the gage. Guidelines for making the determination are found below:
  The measurement system is acceptable if the Gage R & R score falls below 10%
  The measurement system may be determined acceptable depending upon the relative importance of the application or other factors if the Gage R & R falls between 10% to 20%
  Any measurement system with Gage R & R greater than 30% requires action to improve
    Any actions identified to improve the measurement system should be evaluated for effectiveness

## Slide 18: How to Perform Measurement System Analysis (MSA)
When interpreting the results of a Gage R & R, perform a comparison study of the repeatability and reproducibility values.
If the repeatability value is large in comparison to the reproducibility value, it would indicate a possible issue with the gage used for the study.
The gage may need to be replaced or re-calibrated.
Adversely, if the reproducibility value is large in comparison with the repeatability value, it would indicate the variation is operator related.
The operator may need additional training on the proper use of the gage or a fixture may be required to assist the operator in using the gage.

## Slide 19: How to Perform Measurement System Analysis (MSA)
Gage R & R studies shall be conducted under any of the following circumstances:
  Whenever a new or different measurement system is introduced
  Following any improvement activities
  When a different type of measurement system is introduced
  Following any improvement activities performed on the current measurement system due to the results of a previous Gage R & R study
  Annually in alignment with set calibration schedule of the gage

## Slide 20: How to Perform Measurement System Analysis (MSA)
Attribute Gage R & R
  Attribute measurement systems can be analyzed using a similar method. Measurement uncertainty of attribute gages shall be calculated using shorter method as below:
  Determine the gage to be studied
  Obtain 10 random samples from a regular production run
  Select 2 different operators who perform the particular inspection activity regularly
  Have the operators perform the inspection two times for each of the sample parts and record the data
  Next, calculate the kappa value.
  When the kappa value is greater than 0.6, the gage is deemed acceptable
    If not, the gage may need to be replaced or calibrated

## Slide 21: How to Perform Measurement System Analysis (MSA)
Attribute Gage R & R
  The attribute gage study should be performed based on the same criteria listed previously for the Gage R & R study.
  During MSA, the Gage R&R or the attribute gage study should be completed on each of the gages, instruments or fixtures used in the measurement system. The results should be documented and stored in a database for future reference. It may be required for a PPAP submission to the customer.
  Furthermore, if any issues should arise, a new study can be performed on the gage and the results compared to the previous data to determine if a change has occurred. A properly performed MSA can have a dramatic influence on the quality of data being collected and product quality.

## Slide 22: Key terms and definitions
Attribute data – Data that can be counted for recording and analysis (sometimes referred to as go/ no go data)
Variable data – Data that can be measured; data that has a value that can vary from one sample to the next; continuous variable data can have an infinite number of values
Bias – Difference between the average or mean observed value and the target value
Stability – A change in the measurement bias over a period of time
A stable process would be considered in “statistical control”
Linearity – A change in bias value within the range of normal process operation
Resolution – Smallest unit of measure of a selected tool gage or instrument; the sensitivity of the measurement system to process variation for a particular characteristic being measured

## Slide 23: Key terms and definitions
Accuracy – The closeness of the data to the target or exact value or to an accepted reference value
Precision – How close a set of measurements are to each other
Repeatability – A measure of the effectiveness of the tool being used; the variation of measurements obtained by a single operator using the same tool to measure the same characteristic
Reproducibility – A measure of the operator variation; the variation in a set of data collected by different operators using the same tool to measure the same part characteristic

## Slide 24: Key terms and definitions
Accuracy – The closeness of the data to the target or exact value or to an accepted reference value
Precision – How close a set of measurements are to each other
Repeatability – A measure of the effectiveness of the tool being used; the variation of measurements obtained by a single operator using the same tool to measure the same characteristic
Reproducibility – A measure of the operator variation; the variation in a set of data collected by different operators using the same tool to measure the same part characteristic

## Slide 25: Measurement Systems Analysis

## Slide 26: Measurement Systems Analysis
Basic Concepts of Measurement Systems
  A Process
Statistics and the Analysis of Measurement Systems
Conducting a Measurement Systems Analysis
ISO - TC 69 is the Statistics Group
Ensures high ‘Data Quality’ (Think of Bias)

## Slide 27: Course Focus & Flow
Measurement as a Process
Mechanical Aspects (vs Destructive)
  Piece part
  Continuous (fabric)
Features of a Measurement System
Methods of Analysis
Gauge R&R Studies
Special Gauging Situations
  Go/No-Go
  Destructive Tests

## Slide 28: Place Timeline Here

## Slide 29: The Target & Goal
Prototype
Pre-Launch
Production
USL
LSL
Continuous Improvement

## Slide 30: Key Words
Discrimination
  Ability to tell things apart
Bias [per AIAG] (Accuracy)
Repeatability [per AIAG] (Precision)
Reproducibility
Linearity
Stability

## Slide 31: Terminology
Error ≠ Mistake
Error ≠ Uncertainty
Percentage Error ≠ Percentage Uncertainty
Accuracy ≠ Precision

## Slide 32: Measurement Uncertainty
Different conventions are used to report measurement uncertainty.
What does ±5 mean in m = 75 ±5?
  Estimated Standard Deviation: 
  Estimated Standard Error: m = /√N
  Expanded Uncertainty of ± 2 or 3
    Sometimes ± 1 (Why?)
  95% or 99% Confidence Interval
  Standard Uncertainty: u
  Combined Standard Uncertainty: uc

## Slide 33: Measurement Uncertainty
Typical Reports
Physici

## Slide 34: Measurement as a Process
Basic Concepts
Components of the Measurement System
Requirements of a Measurement System
Factors Affecting a Measurement System
Characteristics of a Measurement System
  Features (Qualities) of a Measurement Number
    Units (Scale)
    Accuracy
    Precision (Consistency or Repeatability)
    Resolution (Reproducibility)

## Slide 35: Measurement Related Systems
Typical Experiences with
Measurement Systems

## Slide 36: Basic Concepts
Every Process Produces a “Product”
Every Product Possesses Qualities (Features)
Every Quality Feature Can Be Measured
Total Variation
  = Product Variation + Measurement Variation
Some Variation Inherent in System Design
Some Variation is Due to a Faulty Performance of the System(s)

## Slide 37: The Measurement Process
What is the ‘Product’ of the Measurement Process?
What are the Features or Qualities of this Product?
How Can We Measure Those Features?

## Slide 38: Measurement Systems Components
Material to be Inspected
  Piece
  Continuous
Characteristic to be Measured
Collecting and Preparing Specimens
Type and Scale of Measurement
Instrument or Test Set
Inspector or Technician
  AIAG calls these ‘Appraiser’
Conditions of Use

## Slide 39: Where Does It Start?
During the Design (APQP) Stage:
The engineer responsible for determining inspections and tests, and for specifying appropriate equipment should be well versed in measurement systems. The Calibration folks should be part of the process as a part of a cross-functional team.
Variability chosen instrument must be small when compared with:
Process Variability
Specification Limits

## Slide 40: Typical Progression
Determine ‘Critical’ Characteristic
Determine What Equipment is Already Available
Determine Required Resolution
Consideration of the Entire Measurement System for the Characteristic
(Variables)
Cross-Functional
Product Engineer
Product Engineer
Metrology
How will the data be used?

## Slide 41: Measurement Systems Variables
Measurement
Instrument
Environment
Material
Inspector
Methods
Sample Preparation
Sample Collection
Parallax
Reproducibility
Training
Practice
Ergonomics
Test Method
Workmanship
Samples
Standards
Discrimination
Repeatability
Bias
Calibration
Linearity
Vibration
Lighting
Temperature
Humidity
These are some of the variables in a measurement system. What others can you think of?
Fixture
Eyesight
Air Pressure
Air Movement
Fatigue

## Slide 42: Determining What To Measure
Voice of the Customer
  You Must Convert to Technical Features
Technical Features
Failure Modes Analysis
Control Plan
Convert To
External Requirements
Internal Requirements

## Slide 43: Voice of the Customer
External and Internal Customers
Stated vs Real and Perceived Needs
Cultural Needs
Unintended Uses
Functional Needs vs. Technical Features
Customer may specify causes rather than output

## Slide 44: Convert to Technical Features
Agreed upon Measure(s)
Related to Functional Needs
Understandable
Uniform Interpretation
Broad Application
Economical
Compatible
Basis for Decisions
Y
Z
Technical Feature
Functional Need

## Slide 45: Failure Modes Analysis
Design FMEA
Process FMEA
Identify Key Features
Identify Control Needs
Critical Features are Defined Here!

## Slide 46: Automotive FMEA
Leading to MSA. Critical features are determined by the FMEA (RPN indicators) and put into the Control Plan.

## Slide 47: Control Plan / Flow Diagram
Inspection Points
Inspection Frequency
Instrument
Measurement Scale
Sample Preparation
Inspection/Test Method
Inspector (who?)
Method of Analysis

## Slide 48: GM Process Flow Chart

## Slide 49: Standard Control Plan Example
This form is on course disk

## Slide 50: Ford’s Dimensional Control Plan (DCP)

## Slide 51: Measurement as a System
Choosing the Right Instrument
  Instrument Calibration Needs
  Standards or Masters Needed
  Accuracy and Precision
Measurement Practices
  Where
  How Many Places
Reported Figures
  Significant Figures Rule
    2 Action Figures
    Rule of 10
  Individuals, Averages, High-Lows

## Slide 52: Measurement Error
Measured Value (y)
=
True Value (x) + Measurement Error
Deming says there is no such thing as a ‘True’ Value.
Consistent (linear)?

## Slide 53: Sources of Measurement Error
Sensitivity (Threshold)
  Chemical Indicators
Discrimination
Precision (Repeatability)
Accuracy (Bias)
Damage
Differences in use by Inspector (Reproducibility)
  Training Issues
Differences Among Instruments and Fixtures
Differences Among Methods of Use
Differences Due to Environment

## Slide 54: Types of Measurement Scales
Variables
  Can be measured on a continuous scale
  Defined, standard Units of Measurement
Attributes
  No scale
  Derived ‘Unit of Measurement’
  Can be observed or counted
  Either present or not
  Needs large sample size because of low information content

## Slide 55: How We Get Data
Inspection
Measurement
Test
Includes Sensory (e.g..: look,
touch, smell…etc)
Magnitude of Quality

## Slide 56: Operational Definitions
Is the container Round?
Is your software Accurate?
Is the computer screen Clean?
Is the truck On Time?

## Slide 57: Different Method = Different Results
In Spec
Out of Spec
Method 1
Method 2

## Slide 58: Measurement System Variability
Small with respect to Process Variation
Small with respect to Specified Requirements
Must be in Statistical Control
  Measurement IS a Process!
  Free of Assignable Causes of variation

## Slide 59: Studying the Measurement System
Environmental Factors
Human Factors
System Features
Measurement Studies

## Slide 60: Environmental Factors
Temperature
Humidity
Vibration
Lighting
Corrosion
Wear
Contaminants
  Oil & Grease
  Aerosols
Where is the study performed?
1. Lab?
2. Where used?
3. Both?

## Slide 61: Human Factors
Training
Skills
Fatigue
Boredom
Eyesight
Comfort
Complexity of Part
Speed of Inspection (parts per hour)
Misunderstood Instructions

## Slide 62: Human Measurement Errors
Sources of Errors
  Inadvertent Errors
    Attentiveness
    Random
    Good Mistake-Proofing Target
  Technique Errors
    Consistent
  Wilful Errors (Bad mood)
Error Types (Can be machine or human)
  Type I - Alpha Errors [ risk]
  Type II - Beta Errors [ risk]
Accept
Reject
Good
Bad
OK!
OK!
alpha
beta
Training Issue
Process in control, but needs adjustment, False alarm
Unaware of problem

## Slide 63: Measurement System Features
Discrimination
  Ability to tell things apart
Bias [per AIAG] (Accuracy)
Repeatability [per AIAG] (Precision)
Reproducibility
Linearity
Stability

## Slide 64: Discrimination
Readable Increments of Scale
If Unit of Measure is too course: Process variation will be lost in Rounding Off
The “Rule of Ten”: Ten possible values between limits is ideal
  Five Possible Values: Marginally useful
  Four or Less: Inadequate Discrimination

## Slide 65: Discrimination

## Slide 66: Range Charts & Discrimination
Indicates Poor Precision

## Slide 67: Bias and Repeatability
Precise
Imprecise
Accurate
Inaccurate
Bias
You can correct for Bias
You can NOT correct for Imprecision

## Slide 68: Bias
Difference between average of measurements and an Agreed Upon standard value
Known as Accuracy
Cannot be evaluated without a Standard
Adds a Consistent “Bias Factor” to ALL measurements
Affects all measurements in the same way
Standard
Value
Measurement Scale
Bias

## Slide 69: Causes of Bias
Error in Master
Worn components
Instrument improperly calibrated
Instrument damaged
Instrument improperly used
Instrument read incorrectly
Part set incorrectly (wrong datum)

## Slide 70: Bias
Bias - The difference between the observed Average of measurements and the master Average of the same parts using precision instruments. (MSA Manual Glossary)
The auditor may want evidence that the concept of bias is understood. Remember that bias is basically an offset from ‘zero’. Bias is linked to Stability in the sense that an instrument may be ‘zeroed’ during calibration verification. Knowing this we deduce that the bias changes with instrument use. This is in part the concept of Drift.

## Slide 71: Bias
I choose a caliper (resolution 0.01) for the measurement. I measure a set of parts and derive the average.
I take the same parts and measure them with a micrometer (resolution 0.001). I then derive the average.
I compare the two averages. The difference is the Bias.

## Slide 72: Repeatability
Variation among repeated measurements
Known as Precision
Standard NOT required
May add or subtract from a given measurement
Affects each measurement randomly
Measurement Scale
Repeatability
Margin of Error
Doesn’t address Bias
5.15 = 99%

## Slide 73: Repeatability Issues
Measurement Steps
  Sample preparation
  Setting up the instrument
  Locating on the part
How much of the measurement process should we repeat?

## Slide 74: Using Shewhart Charts I
Repeatability

## Slide 75: Using Shewhart Charts II

## Slide 76: Evaluating Bias & Repeatability
Same appraiser, Same part, Same instrument
Multiple readings (n≥10 with 20 to 40 better)
Analysis
  Average minus Standard Value = Bias
  5.15* Standard Deviation = Repeatability
  or +/- 2.575  [99% repeatability]
  or +/- 2  [95% repeatability]
Histogram
Probability
AIAG

## Slide 77: Repeatability Issues
Making a measurement may involve numerous steps
  Sample preparation
  Setting up the instrument
  Locating the part, etc.
How much of the measurement process should we repeat? How far do we go?

## Slide 78: Bias & Repeatability Histogram
Never include assignable cause errors

## Slide 79: Linearity
The difference in the Bias or Repeatability across the expected operating range of the instrument.

## Slide 80: Plot Biases vs. Ref. Values
Linearity = |Slope| * Process Variation = 0.1317*6.00 = 0.79
% Linearity = 100 * |Slope| = 13.17%

## Slide 81: Causes of Poor Linearity
Instrument not properly calibrated at both Upper and Lower extremes
Error in the minimum or maximum Master
Worn Instrument
Instrument design characteristics

## Slide 82: Reproducibility
Variation in the averages among different appraisers repeatedly measuring the same part characteristic
Concept can also apply to variation among different instruments
Includes repeatability which must be accounted for.

## Slide 83: Reproducibility Example

## Slide 84: Calculating Reproducibility (I)
Find the range of the appraiser averages (R0)
Convert to Standard Deviation using d2*
  (m=# of appraisers; g=# of ranges used = 1)
Multiply by 5.15
Subtract the portion of this due to repeatability

## Slide 85: Calculating Reproducibility
People variance
Trials
Times done

## Slide 86: Stability
Variation in measurements of a single characteristic
On the same master
Over an extended period of time
Evaluate using Shewhart charts

## Slide 87: Evaluate Stability with Run Charts

## Slide 88: Stability
Both gages are stable, but.....

## Slide 89: Importance of Stability
Statistical stability, combined with subject-matter knowledge, allows predictions of process performance
Action based on analysis of Unstable systems may increase Variation due to ‘Tampering’
A statistically unstable measurement system cannot provide reliable data on the process

## Slide 90: Methods of Analysis

## Slide 91: Analysis Tools
Calculations of Average and Standard Deviation
Correlation Charts
Multi-Vari Charts
Box-and-Whisker Plots
Run charts
Shewhart charts

## Slide 92: Average and Standard Deviation

## Slide 93: Correlation Charts
Describe Relationships
Substitute measurement for desired measurement
Actual measurement to reference value
Inexpensive gaging method versus Expensive gaging method
Appraiser A with appraiser B

## Slide 94: Substitute Measurements
Cannot directly measure quality
Correlate substitute measure
Measure substitute
Convert to desired quality

## Slide 95: Comparing Two Methods
Two methods
Measure parts using both
Correlate the two
Compare to “Line of No Bias”
Investigate differences
Magnetic
Stripping
Line of Perfect Agreement
Line of Correlation

## Slide 96: Measurements vs. Reference Data

## Slide 97: Measurements vs. Reference Correlation
Disparity

## Slide 98: Comparing Two Appraisers

## Slide 99: Run Charts Examine Stability

## Slide 100: Multiple Run Charts
More than 3 appraisers confuses things...

## Slide 101: Multi-Vari Charts
Displays 3 points
Length of bar; bar-to-bar; Bar cluster to cluster
Plot High and Low readings as Length of bar
Each appraiser on a separate bar
Each piece in a separate bar cluster
High Reading
Low Reading
Average Reading

## Slide 102: Multi-Vari Type I
Bar lengths are long
Appraiser differences small in comparison
Piece-to-piece hard to detect
Problem is repeatability

## Slide 103: Multi-Vari Type II
Appraiser differences are biggest source of variation
Bar length is small in comparison
Piece-to-piece hard to detect
Problem is reproducibility

## Slide 104: Multi-Vari Type III
Piece-to-piece variation is the biggest source of variation
Bar length (repeatability) is small in comparison
Appraiser differences (bar-to-bar) is small in comparison
Ideal Pattern

## Slide 105: Multi-Vari Chart Example
Normalized Data

## Slide 106: Multi-Vari Chart, Joined
Look for similar pattern

## Slide 107: Using Shewhart Charts
Subgroup = Repeated measurements,, same piece
Different Subgroups = Different pieces and/or appraisers
Range chart shows precision (repeatability)
Average chart “In Control” shows reproducibility
  If subgroups are different appraisers
Average chart shows discriminating power
  If subgroups are different pieces
(“In Control” is BAD!)

## Slide 108: Shewhart Charts
This is not a good way to plot this data
Too many lines

## Slide 109: Shewhart Chart of Instrument

## Slide 110: Gage R&R Studies

## Slide 111: Gauge R&R Studies
Developed by Jack Gantt
Originally plotted on probability paper
Revived as purely numerical calculations
Worksheets developed by AIAG
Renewed awareness of Measurement Systems as ‘Part of the Process’
Consider Numerical vs. Graphical Data Evaluations

## Slide 112: Terms Used in R&R (I)
n = Number of Parts [2 to 10]
  Parts represent total range of process variation
  Need not be “good” parts. Do NOT use consecutive pieces.
  Screen for size
a = Number of Appraisers
  Each appraiser measures each part r times
  Study must be by those actually using
R - Number of trials
  Also called “m” in AIAG manual
g = r*a [Used to find d2* in table 2, p. 29 AIAG manual]
1 Outside Low/High
1 Inside Low/High
Target
Minimum of 5.
2 to 10 To accommodate worksheet factors
1
2
3
4
5

## Slide 113: Terms Used in R&R (II)
R-barA = Average range for appraiser A, etc.
R-double bar = Average of R-barA, R-barB
Rp = Range of part averages
XDIFF = Difference between High & Low appraiser averages
  Also a range, but “R” is not used to avoid confusion
EV = 5.15 = Equipment variation (repeatability)
EV = 5.15 = Equipment variation (reproducibility)
PV = Part variation
TV = Total variation
Process Variation

## Slide 114: R&R Calculations
Measurement System Variation
Product Process Variation
Left over Repeatability
Remember - Nonconsecutive Pieces
Left over Repeatability

## Slide 115: Accumulation of Variances

## Slide 116: Evaluating R&R
%R&R=100*[R&R/TV] (Process Control)
%R&R=100*[R&R/Tolerance] (Inspection)
Under 10%: Measurement System Acceptable
10% to 30%: Possibly acceptable, depending upon use, cost, etc.
Over 30%: Needs serious improvement

## Slide 117: Analysis of Variance I
Mean squares and Sums of squares
Ratio of variances versus expected F-ratio
Advantages
  Any experimental layout
  Estimate interaction effects
Disadvantages
  Must use computer
  Non-intuitive interpretation

## Slide 118: Analysis of Variance II
The n*r measurements must be done in random sequence [a good idea anyway]
Assumes that EV [repeatability] is normal and that EV is not proportional to measurement [normally a fairly good assumption]
Details beyond scope of this course

## Slide 119: Special Gauging Situations
Go/No-Go
Destructive Testing

## Slide 120: If Gauges were Perfect

## Slide 121: But Repeatability Means We Never Know The Precise Value

## Slide 122: So - Actual Part Acceptance Will Look Like This:

## Slide 123: The Effect of Bias on Part Acceptance

## Slide 124: Go/No-Go gauges
Treat variables like attributes
Provide less information on the process, but...
Are fast and inexpensive
Cannot use for Process Control
Can be used for Sorting purposes

## Slide 125: “Short” Go/No-Go Study
Collect 20 parts covering the entire process range
Use two inspectors
Gage each part twice
Accept gauge if there is agreement on each of the 20 parts
* May reject a good measuring system

## Slide 126: Destructive Tests
Cannot make true duplicate tests
Use interpenetrating samples
Compare 3 averages
Adjust using √n

## Slide 127: Destructive Tests: Interpreting Samples
AIAG does not address

## Slide 128: Summary

## Slide 129: Measurement Variation
Observed variation is a combination of the production process PLUS the measurement process
The contribution of the measurement system is often overlooked

## Slide 130: Types of Measurement Variation
Bias (Inaccuracy)
Repeatability (Imprecision)
Discrimination
Linearity
Stability

## Slide 131: Measurement Systems
Material
Characteristic
Sampling and Preparation
Operational Definition of Measurement
Instrument
Appraiser
Environment and Ergonomics

## Slide 132: Measurement Systems Evaluation Tools
Histograms
Probability paper
Run Charts
Scatter diagrams
Multi-Vari Charts
Gantt “R&R” analysis
Analysis of Variance (ANOVA)
Shewhart “Control” Charts

## Slide 133: Shewhart Charts
Range chart shows repeatability
X-bar limits show discriminating power
X-double bar shows bias
  (if a known standard exists)
Average chart shows stability
  (sub-groups overtime)
Average chart shows reproducibility
  (sub-groups over technicians/instruments)

## Slide 134: Conclusion
Rule of Ten
Operating Characteristic Curve
Special Problems
  Go/No-Go Gages
  Attribute Inspection
  Destructive Testing